## Slide 1
Aqara Smart Curtain Controller Introduction

## Slide 2
Content
Product introduction
Product installation
Configuration on App
FAQ

## Slide 3
Product Profile
Aqara Curtain Controller is a ZigBee wireless communication protocol based, using ultra-quiet DC motor, with resistance to stop, stops when pull by hand and other characteristics, with ZigBee hub function with the device (referred to as "hub"), can achieve remote control, timer switch and devices, smart linkage and other functions.
Please scan the QR code to watch the product video.
*This product is for indoor use only. Please bind the product to the Hub before use.
*Aqara Hub is required to enable Aqara Smart Curtain Controller to work with Homekit.
One-click Control
Remote Control
Schedules
Custom Percentage
Reset Button
Indicator

## Slide 4
Smart Curtain Controller Usages
Aqara smart curtain controller can be used at home/office/hotel and so on.
Usage 1:
Your curtain will close automatically in case you go out.
Usage 2:
Use your Aqara Hub M1S as an illumination sensor to adjust your curtain dynamically.
Usage 3:
Control the curtain using the configurable gestures of the Aqara Cube or any other compatible wireless controller.

## Slide 5
Product Selling Points
Customize Opening/Closing Position
You can save your favorite opening percentages via smart scenes and switch between them easily.
All-Round Compatibility
Supports the most popular voice assistants and ecosystems.
Schedules
Your shades will open and close at a specified time of the day, for example, right before your alarm clock.
Smart Home Automation
Can be triggered by sensors such as Illumination, Motion, Door and Window Sensor, and more.
Multiple Control
Can be fully controlled by a single button such as the Wireless Mini Switch. And also support control manually.
Various Curtain Mode
Apart from opening both, it also supports open left curtain and open right curtain.

## Slide 6
Product Specifications
Specifications | Zigbee Version
Model | ZNCLDJ11LM
Supply Voltage | 100-240V~50/60Hz
Cable Length | 1 meter（Plug is excluded）
Noise | Around 30dB
Torque | 1.2N·m
Dimensions: | 70 x 50 x 346 mm
Protection Standard | IP40
Weight | 1.5 kg
Opening Speed | 14cm/s
Max Load | 50KG
Communication Protocol | Zigbee
Operating Temperature | -20°С +55°С
Operating Humidity | 10% - 90%RH，non-condensing
Power | 13W
Package Contents | Motor, User Manual.

## Slide 7
Button Functions
Reset button
Long press for 5s: Reset/Add the device;
Single press: Effective range test/Device identify;
Indicator light
Effective range test: When single press the reset button, the Hub will make voice prompt of “Normal link confirmed” , it means the connection between the device with Hub is normal.
Device identify: When single press the reset button, the device will flash on the app at the menu of Accessories.
.

## Slide 8
Indicator Functions
No. | LED indication | Implication
1 | Blue light flash once | Power on, the blue light flashes once
2 | Blue light always on | Connected, motor is running
3 | Blue light continues to flash quickly | Connecting
4 | Red light flashes slowly | Not connected (or reset to factory)

## Slide 9
Content
Product introduction
Product installation
Configuration on App
FAQ

## Slide 10
Product Installation
Please watch the installation video from the link below:
https://cdn.cnbj2.fds.api.mi-img.com/cdn/single-h5/Channel/aqaradetails/aqaracurtain.html?v=20180926

## Slide 11
Product Installation- Measure Preparation
Installation Environment
Roughcast House
Gypsum Ceiling
Customized(Curved) Window
Roman Rod

## Slide 12
Product Installation- Measure Preparation
Measure Preparation
Screwdriver
Test Pencil
Pencil
NoteBook
Tapeline

## Slide 13
Product Installation- Measure Preparation
Measurement Method
Please confirm with customer it is whole wall installation
or not before measurement.
L Shape Track
Straight Track
whole wall
non-whole wall
L Shape Track
Left
Right
Measure: AB, BC
Note:
1. Track is a customized product that cannot be returned or replaced
2. Roma rod is not support. It need to be demolished if already install and replace it with the curtain(open and close from left and right).
3. Measurement should be performed after the customer finishes the decoration instead of before it.
4. Hollow wall and gypsum board are not solid enough to support. Please ensure the wall is firm enough to insall the curtain controller, like the walls made up of carpentry board or stone.

## Slide 14
Product Installation- Measure Preparation
Power Source/Socket Preparation
Note: Curtain controller comes with 1m power wire(no plug included). If there is no 10A power socket existing nearby, customer need to prepare extension wire themselves.
Curtain controller can be installed either on the left or right, which is depended on customer's preference.
Single-layer curtain
*one power socket required
Double-layer curtain
*Two power sockets required

## Slide 15
Product Installation
Power Source/Socket Preparation

Curtain motor comes with a 1m long power cord (plug is excluded). If there is no reserved power cord or 10A socket on one side of the shutter motor in the home, the user needs to prepare the extension cord or have the installer assist to connect the home power cord directly with the motor power cord for use.
Single Curtain Motor
1 Power socket is required to be reserved.
Dual Curtain Motor (1 Cloth +1 Sheer Curtain)
2 Power socket is required to be reserved.

## Slide 16
Product Installation- Measure Preparation
Installation Method
One way
Two way
1*lazy arm
2*lazy arm
Ceiling mounting
(with curtain box )
*It can be mounted on the ceiling with/without curain box
Wall Mounting
(without curtain box )
*Mounting with curtain box is not permitted

## Slide 17
Product Installation- Measure Preparation
Measure Curtain Box
Single Straight Track
Inner diameter＞10cm
Double Straight Track
Inner diameter＞20cm
Single L Track
Inner diameter＞20cm
Double L Track
Inner diameter＞30cm

## Slide 18
Product Installation
Installation Preparation
Before Installation:
1. Check if the number of the controller and track, make sure they match the customer's requirement.
2. Make sure the controller and track are not damaged due to transportation.
3. Power on the controller tp confirm if it works properly.
4. Measure the track's dimesion and check whether it matches the original data or not.
Plier
Electrical Tape
Hammer Drill
Tapeline
Ladder
Screwdriver
Test Pencil
Pencil
Notebook
Cutter

## Slide 19
Product Installation
Ceiling Mounting
Ceiling material supports installation-- it needs to be determined by the installer or user whether it can bear the load.
Note: Ceiling Mounting (With Curtain Box)
1. Can be installed W/WO curtain box
2. The depth of curtain box is recommended to be less than 15cm
With Curtain Box

## Slide 20
Product Installation
Side Mounting (No Curtain Box)
The side mounting surface shall be greater than 7cm (the requirements for monorail and double rail are the same).
Side Mounting (No Curtain Box)
*Can be installed only without curtain box

## Slide 21
Product Installation
Reserved size of curtain slot
Straight Monorail 10CM Straight dual rail 20CM L Shape monorail 20CM L Shape dual rail 30CM

## Slide 22
Product Installation
Curtain Requirement
1. The curtain requires hooks due to the curtain track is hung by the circular hanging ring.
2. The weight of curtain shall not exceed 50KG.

## Slide 23
Content
Product introduction
Product installation
Configuration on App
FAQ

## Slide 24
How to Bind Curtain Controller on App
Open the app, enter “Add Accessory” and select “Curtain controller” .
Press and hold the reset button for more than 5s, until the blue light is on.
Click “Done” to complete the device binding.
1
2
3
4
5
6
Choose a Hub. Please complete the hub binding before selecting a hub here.

## Slide 25
How to Rename the Device
2
3
1
4
Open the app, enter “Accessories” and select “Curtain controller” .
Click “...” .
Input new name and click “Confirm”.
*Once rename the device, the new name will display at the menu of “Accessories” on App.
5
Click “Accessory Name” .

## Slide 26
1
Enable “Add it to Favorites”.
Give the new name on the homepage for device as per requirement.
2
How to Add Device to “Favoriate” on Homepage
Open the app, enter “Curtain controller” . Then click ”Homepage Card”.
3
Go to the homepage and click “Favorites”. The device will display here.
4
5
6
*Once give the new name at step 3, the new name will display at “Favoriate”.

## Slide 27
Select the location: Step 1--Step 2;
Create new location: Step 1--Step 3--Step 4--Step 5, or you can select the name in the list here;
Select the wallpaper: Step 1--Step 3--Step 6--Step 7.
1
2
3
4
5
6
7
How to Set Location

## Slide 28
How to Identify the Device
Single press the reset button.
Check the device at the “Accessories” Page. The device will flash on App.
1
2

## Slide 29
How to Control the Curtain on APP
Button to open/stop/close the curtain
Button to control the percentage of the opening/closing

## Slide 30
1
2
How to Select Curtain Mode
Click “More Settings”
Click “Curtain Mode”
Select the curtain mode from the list

## Slide 31
How to Set Open/Close Curtain Manually
1
2
Click “More Settings”
Enable “Open/Close Curain Manually”

## Slide 32
1
2
How to Set Open/Close Curtain in Reverse Direction
Click “More Settings”
Enable “Open/Close Curtain in Reverse Direction”

## Slide 33
1
2
How to Create Device Group
Click “Create a device group”
Select the device and click “Next” to complete the setting.
3

## Slide 34
1
2
How to Check Logs
Click “Logs” when enter “Curtain controller”.
Select the date.

## Slide 35
How to Configure Automation and Scene
IF:
Not support
Aqara curtain controller supports the below Automation on Aqara Home App.
Please click “Automation” and “Scene” to start the configuration, below are the main steps on App.
Then:
Open
Close
Open/Close
Open to
Stop
Adjust curtain opening ratio (Only support cube rotation)
Set it to specified scene
Automation configuration
Scene configuration

## Slide 36
Content
Product introduction
Product installation
Configuration on App
FAQ

## Slide 37
FAQ for Curtain Controller
1. What is the maximum load the Aqara Curtain Controller supports?
50KG
2. How much is the torque of the Aqara Curtain Controller?
1.2N·m
3. When I pull the curtain manually, the curtain can not open or close automatically.
Please make sure that the "Open/close curtain manually" feature is enabled already in the app.
4. How to reset the Aqara Curtain Controller?
Please long-press the reset button for 5 seconds until the blue indicator light goes on and release it.
5. The curtain stopped halfway.
1. Please check if there are obstacles on the curtain track.
2. Clear the motor's route by the “Clear route” command in the app, and then try again.
6. Can the curtain be opened/closed after the Aqara Curtain Controller powers off?
Aqara Curtain Controller supports the " Manual" feature. The curtain can be opened/closed manually after the motor powers off.
7. If the curtain will close when we control the device to open it and vice versa, how could we adjust it to the correct direction?
Please adjust the direction through "Adjust opening/closing direction of curtain" in "Settings" in the app.

## Slide 38
Thank you